## Slide 1
Unveil the Relationship Between Process and Design Embedded in the 3D Point Cloud using Unsupervised Learning
Department of Industrial and Systems Engineering
Evans Nyanney
Faculty Advisor: Geng Zhaohui
Investigate : Variational patterns in 3D point cloud data related to geometric design and additive manufacturing processes.
Characterize: Key (local) geometric features influencing point cloud accuracy and precision in 3D printed objects.
Link process and design: Reveal the relationship between geometric design and the accuracy and precision of the corresponding additive manufactured parts.
Local PGA pipeline: Develop an unsupervised method to model the local variance and capture the geometric variational patterns.
Data Acquisition & Normalization: Collect 3D scans; standardize or min–max scale coordinates
Spectral Clustering: Build an affinity matrix, compute the Laplacian, then apply eigen-decomposition and k-means.
Label Alignment: Use the Hungarian algorithm to match cluster labels across scans.
Local PGA: Project clusters onto a tangent space; run PCA to extract principal geodesics and map them back.
Variance Validation: Apply Kruskal–Wallis for variance checks; use ARI/NMI to assess clustering stability
We evaluated scans of two 3D printed objects—a half-ball and a free-form structure—made with a LulzBot TAZ 3D printer using 2.85” polymer filament.
Half-Ball Freeform
Figure 5: The CAD models and physical objects considered in our study.
Manufacturing signatures: The PGA pipeline segments 3D point clouds into clusters that highlight specific process variations.
Geometry-process mapping: Grouping geometric features links raw structure to manufacturing variations for targeted quality improvements..
Figure 6: Visualization of the pointwise deviations with different layer thick-ness
Robust variance capture: The Local PGA pipeline effectively segments point clouds, revealing localized geometric variability validated by statistical tests and consistent clustering.
Future integration: Future work will link these variations to manufacturing quality and integrate defect detection for enhanced process control.
Local PGA pipeline: Develop an unsupervised method to model the local variance and capture the geometric variational patterns.
Figure 1: Average Variance for each cluster (Half-Ball).
Figure 2: Average Variance for each cluster (Freeform).
Figure 3: Variance Distribution Across Clusters for Half-Ball.
Figure 4: Variance Distribution Across Clusters for Freeform.
Table 1: Variance Analysis for Half-Ball and Freeform Measurements
Table 2: Clustering Consistency Metrics Comparison (Overall, not axis-specific